## Slide 1: Assignment1

## Slide 2: Iperf TCP throughput
Chart: TCP throughput
| basic | half window | parallel
wire | 373 | 347 | 349
wireless | 171 | 70 | 185
Observe and plot TCP throughput over the wired/wireless channel using different parameters of iPerf
Mb/s

## Slide 3: Parallel Connections
Parallel connection bandwidth is smaller than basic connections. More parallel cannot increase bandwidth in a wired environment.
Explain:
Multiple connections can potentially lead to increased overhead and resource utilization, so the sum bandwidth is smaller than the basic connection.

## Slide 4: Bandwidth vs TCP window size
The bandwidth increases with the window size increase
Explain:
Increasing the TCP window size to half means the sender can send more unacknowledged packets before pausing, resulting in a higher data transmission rate and increased bandwidth.
On the contrary, smaller window sizes lead to increased acknowledgment overhead and less efficient network capacity utilization, causing a decrease in bandwidth.

## Slide 5: Wireless（ WiFi）
Wired networks use physical cables, providing stable and interference-free communication, while wireless networks rely on radio waves, which are susceptible to interference and signal degradation.
Shared wireless channels, signal attenuation over distance, and half-duplex communication further limit wireless bandwidth.

## Slide 6: Different Location
The different server has different bandwidth
USA
KAUST

## Slide 7: Delay vs link rate
Chart: Link rate
| link rate
My laptop | 436
KAUST server | 718
LA server | 1527
Mb/s
Chart: Delay
My laptop | 2
KAUST server | 4
LA server | 317 | 320
ms
Chart: Ttl hop
| ttl hop kaust server | ttl hop my laptop
My laptop | 58
KAUST server | 63
LA server | 50 | 54
Because LA server is far away from KAUST. So the delay is much larger.
hop

## Slide 8
Twping localhost